## Slide 1: CCD 415 Project Phase I
Department of Computer Science & Engineering
First Review
SECURE REMOTE NETWORK ACCESS USING TWIN GATE AND RASPBERRY PI
Guided By,
Ms. FARBEENA N
Assistant Professor Department of CSE
Project Members
AKSHAY N(JCE23CC008)
ABHISHEK KB(LJCE23CC034)
SHANID ALI(JCE23CC027)
Project Group No. :08

## Slide 2: OUTLINE
Dept. of CSE
Abstract
Introduction
Problem Definition
Objectives
Background
Literature Survey
Comparative Analysis
Proposed System
Project Planning & Scheduling
Resource/Task Identification & Allocation
Conclusion
References

## Slide 3: ABSTRACT
Dept. of CSE-CC
Secure remote network access is essential for connecting users to private network resources while maintaining strong security and access control.
Traditional remote access methods such as Virtual Private Networks (VPNs) may require firewall modifications, port forwarding, public IP addresses, and complex network configurations, increasing deployment complexity and potential security risks.
A Raspberry Pi is configured as a network connector for Twingate, enabling remote devices to securely access authorized internal resources.
Twingate provides cloud-based management, authentication, device verification, granular access policies, and activity logging.

## Slide 4: INTRODUCTION
Dept. of CSE-CC
Secure remote access enables users to connect to private network resources from different locations while maintaining confidentiality and controlled access.
Traditional network access methods often provide broad connectivity once a user enters the network. Zero Trust improves security by continuously verifying users and devices before granting access.
Twingate provides a Zero Trust Network Access approach that uses identity-based authentication and least-privilege policies to provide access only to authorized resources.
A Raspberry Pi can function as a lightweight network connector, linking internal network resources with the Twingate platform without requiring complex network infrastructure.
Cloud-based management, device verification, access policies, and activity logging help administrators control and monitor remote access securely.
Integration with the Twingate API and Python-based automation can reduce manual configuration, support dynamic resource registration, and simplify network administration.

## Slide 5: PROBLEM DEFINITION
Dept. of CSE-CC
Traditional VPN-based remote access often requires firewall modifications, port forwarding, public IP addresses, and complex network configurations, making deployment difficult.
Conventional remote access methods may provide users with wider network access than necessary, increasing the risk of unauthorized access to internal resources.
Villagers have no advance, location-specific warning, so unfamiliar or nighttime routes can pass directly through a danger zone.
RRT members currently have no prior information (animal type, distance, movement direction) before reaching the site, delaying an informed response.
There is no historical record of intrusion patterns, so hotspots and risk trends cannot be identified or planned for.
Hence, there is a need for a system that automatically detects, verifies, scores, and routes wildlife-intrusion alerts to the right people at the right time.

## Slide 6: OBJECTIVES
Dept. of CSE-CC
To design a thermal-sensor network that continuously monitors identified
wildlife-intrusion hotspots along village boundaries.
To develop an AI/computer-vision module that verifies genuine animal detections and filters out false alarms.
Internal network services may need to be exposed or made reachable from the internet, increasing the potential attack surface and security risks.
Managing users, devices, permissions, and network resources manually can become complex, especially when multiple users require different levels of access.
Traditional approaches may lack simple centralized mechanisms for authentication, access policies, device verification, and monitoring of remote connections.

## Slide 7: BACKGROUND
Dept. of CSE-CC
Background
The increasing need to access private network resources remotely has created a demand for secure and reliable remote connectivity solutions.
VPN-based solutions commonly depend on firewall configuration, port forwarding, public IP addresses, and other network settings that can make deployment more complex.
Zero Trust follows the principle of verifying users and devices before granting access rather than automatically trusting devices within a network.
Twingate applies identity-based authentication and least-privilege access to ensure that users are provided access only to authorized network resources.
The Raspberry Pi provides a low-cost and lightweight platform that can connect internal network resources to the Twingate environment.
Non-lethal deterrents (lights, sound) are an accepted, Forest-Department-approved method for discouraging animals without harm.

## Slide 8: BACKGROUND
Dept. of CSE-CC
Existing System
Remote users commonly rely on VPNs to connect to private network resources from outside the organization.
VPN deployment may require firewall changes, port forwarding, public IP addresses, and additional network configuration.
Once connected through a traditional VPN, users may receive access to a larger portion of the internal network than actually required.
Exposing network services or opening ports for remote access can increase the possibility of unauthorized access and security threats.
Managing users, devices, permissions, and network resources can require considerable manual configuration and administration.
Traditional solutions may make it difficult to implement centralized identity verification, granular access policies, device verification, and activity monitoring.

## Slide 9: LITERATURE SURVEY
Dept. of CSE-CC
R. Tuyishime, F. Radu, E. Tuyishime, D. Cotfas, P. Cotfas, T. Balan, and A. Rekeraho, “Online Laboratory Access Control With Zero Trust Approach: Twingate Use Case,” 2024
Core Methodologies & Algorithms | Advantages | Limitations | Summary
Uses Zero Trust Network Access (ZTNA) for secure remote access. Implements least-privilege access to restrict users to required resources. Uses continuous authentication and authorization for access requests. Uses Raspberry Pi 4B as a network connector. Provides continuous network monitoring and logging. | Improved Access Control: Provides granular access to individual resources instead of exposing the entire network. Reduced Attack Surface: Least-privilege access limits the resources available to an authenticated user. Continuous Monitoring: Network connections are monitored and logged to help identify suspicious activities. | Dependency on Authentication: Access to resources depends on successful authentication and authorization. Connector Dependency: Resources cannot be accessed when the required connector is unavailable. Deployment Complexity: Implementing Zero Trust requires configuration of policies, authentication, connectors, and resource permissions. | Objective: Proposes a Zero Trust Network Access (ZTNA) approach to enable secure remote access to online laboratory environments Mechanism: Applies least-privilege policies using a Raspberry Pi 4B as a lab network connector. Output: Limits user access strictly to required resources, minimizing the lab's attack surface..

## Slide 10: LITERATURE SURVEY
Dept. of CSE-CC
M. Akhi, C. Eising, and L. L. Dhirani, "Securing IoT Using Lightweight TCN for Edge Deployment on Raspberry Pi 4," IEEE Open Journal of the Communications Society, vol. 7, pp. 1184–1200, 2026
Core Methodologies & Algorithms | Advantages | Limitations | Summary
Lightweight TCN Architecture: Uses a 1D Temporal Convolutional Network with causal padding, dilated convolutions (rates 1, 2, 4), batch normalization, $L_2$ regularization, Gaussian noise injection, and Global Average Pooling 1D Post-Training INT8 Quantization: Converts floating-point (FP32) models into full-integer (INT8) TensorFlow Lite (.tflite) representations using representative dataset calibration. Data Processing Pipeline: Applies $z$-score standardization, removal of non-finite values, synthetic class balancing via SMOTE on training data, and 3D temporal tensor reshaping ($N \times F \times 1$) | High Detection Accuracy: Achieves 99.95% accuracy on MQTT-DDoS and 99.94% accuracy on UDP-DDoS datasets Ultra-Low Latency: Delivers inference speeds of 0.19 ms/sample for MQTT-DDoS and 0.27 ms/sample for UDP-DDoS on physical Raspberry Pi 4 hardware. Significant Footprint Compression: Reduces model file size by nearly $4\times$ (from 248.5 KB to 89.1 KB) via INT8 quantization. | Reduced Multi-Class Generalization: Performance drops significantly on highly complex, overlapping Industrial IoT traffic (65.80% accuracy on CICIIoT2025). Hardware Scope Restriction: Evaluated exclusively on single-board computer edge hardware (Raspberry Pi 4) rather than ultra-constrained microcontrollers. .Deployment Threat Vulnerabilities: Remains vulnerable to physical edge threats such as model extraction | Objective: Establishes a lightweight, edge-deployable deep learning Intrusion Detection System (IDS) to mitigate real-time DDoS threats on resource-constrained IoT devices Mechanism: Converts a dilated 1D Temporal Convolutional Network to an INT8-quantized TFLite model running locally on a Raspberry Pi 4 using multi-threaded acceleration.

## Slide 11: LITERATURE SURVEY
Dept. of CSE-CC
N. N. Hari et al., "Standards-Compliant Zero Trust Framework-Based Software-Defined Perimeter (SDP) for Securing Residential IoT Networks," IEEE Transactions on Consumer Electronics, vol. 72, no. 1, pp. 1312–1327, Feb. 2026
Core Methodologies & Algorithms | Advantages | Limitations | Summary
MUD-to-ACL Translation: Fetches MUD JSON profiles via DHCP Option 161/162 or LLDP, verifies digital signatures, and automatically parses allowed endpoints into per-device firewall chains. Ephemeral Overlay Tunnels: Instantiates dynamic, per-session WireGuard encrypted tunnels bound strictly to validated flows. Two-Stage Inter-Device Validation: Intercepts lateral traffic, checking MUD permissions in Stage 1 and evaluating real-time session posture/SPA context in Stage 2. | Ultra-Compact Model: Stage 2 footprint is only 675 kB with 19 ms detection time and ~3-second mobile alert latency.. Modular Species Adaptability: Two-stage setup allows adapting to new wildlife species by retraining Stage 2 only Redundant Alert Channels: Pushes SMS, Push notifications, local audio alarms, and home automation voice alerts to prevent network failure. | Loss of Color Details: Preprocessing converts input frames to 100x100 grayscale before Stage 2 classification.. Cloud & Network Dependency: Delivering SMS/Push alerts relies on cellular connectivity and AWS SNS cloud services.. High Synthetic Ratio: Relies heavily on augmented images (8,306 generated images out of 12,737 total) due to limited raw | Objective: Proposes 'WildlifeNet' to protect communities from dangerous wildlife encounters (e.g., coyotes). Mechanism: Pairs MobileNet SSD object detection with a compact custom CNN classifier on low-cost Raspberry Pi 4 hardware. Output: Delivers rapid mobile notifications within 3 seconds and utilizes recipient feedback for ongoing model optimization.

## Slide 12: LITERATURE SURVEY
Dept. of CSE-CC
S. M. Zohaib, S. M. Sajjad, Z. Iqbal, M. Yousaf, M. Haseeb, and Z. Muhammad, "Zero Trust VPN (ZT-VPN): A Systematic Literature Review and Cybersecurity Framework for Hybrid and Remote Work," Information, 2024.
Core Methodologies & Algorithms | Advantages | Limitations | Summary
Zero Trust Integration: Merges ZTNA principles with traditional VPN infrastructure. Three-Tier Enforcement: Utilizes Policy, Identity, and Security Enforcement Points (PEP, IEP, SEP). Multi-Layered Verification: Combines continuous identity/device checks with SASE, SD-WAN, and encrypted tunneling. Adaptive Risk Assessment: Evaluates real-time contextual data over static single-point logins. | Prevents Lateral Movement: Eliminates implicit trust via continuous posture checks. Enhanced Threat Protection: Secures remote access and prevents data leakage. Performance Optimization: Resolves enterprise VPN latency and scalability bottlenecks Broad Framework Coverage: Bridges legacy access systems with modern cloud security architectures. | High Deployment Complexity: Requires reconfiguring legacy systems and complex ZTNA policies. Resource Overhead: Continuous checks increase computational and authenticationload. Identity Infrastructure Reliance: Depends heavily on external IdPs and device management tools. | Objective: Resolves traditional enterprise VPN latency and security flaws for remote/hybrid work. Mechanism: Combines ZTNA, SASE, and enforcement points (PEP, IEP, SEP) for continuous verification.Output: Delivers least-privilege access, better performance, and enhanced data privacy.

## Slide 13: LITERATURE SURVEY
14
Dept. of CSE-CC
D. N. Jha, G. Lenton, J. Asker, D. Blundell, M. Higgins, and D. C. H. Wallom (2023). "A Run-Time Framework for Ensuring Zero-Trust State of Client’s Machines in Cloud Environment."
Core Methodologies & Algorithms | Advantages | Limitations | Summary
Extended IMA Monitoring: Captures system/process metrics in real time via memory buffers and file hashing. Adaptive Verification Lists: Filters critical directories using Include, Exclude, and Allow lists to optimize data processing. TPM Chain of Trust: Extends PCR registers (pcrextend) to build digests and signs measurement batches. Three-Phase Verification: Validates machine identity, cryptographic signatures, and file hash matches sequentially. | Internal Threat Detection: Catches unauthorized administrative alterations and internal attacks bypassing firewalls. Tamper-Proof Integrity: Uses cryptographic chains to prevent log manipulation or state rollback. Fast & Scalable: Processes machine state within 35.6s for up to 128 concurrent clients. | Irrecoverable Locking: Cryptographic failures lock client machines permanently into an Untrusted state. Virtual TPM Vulnerability: SWTPMs in public clouds lack physical hardware security unless shielded by SGX. | Zero-Trust State Validation: Proposes the TPC framework to continuously track cloud machine integrity at run-time. Distributed Setup: Pairs client-side agents (Kernel, Trust Agent, TPM) with a centralized Verification Cluster Cloud Safeguard: Reduces dwell time by detecting run-time vulnerabilities across cloud VMs and containers..

## Slide 14: LITERATURE SURVEY
Dept. of CSE-CC
K. A. Abuhasel (2023). "A Zero-Trust Network-Based Access Control Scheme for Sustainable and Resilient Industry 5.0."
Core Methodologies & Algorithms | Advantages | Limitations | Summary
Uses Raspberry Pi, PIR sensor, ultrasonic sensor, and camera together. Uses an improved YOLOv5 + CNN model for object detection. Uses image resizing, normalization, and noise removal. Processes data locally on the Raspberry Pi without cloud support. Provides real-time alerts using a buzzer, LED, and LCD. Tested using the DCSASS dataset with 16,853 videos. | .High accuracy: 96.8%. Fast detection: 0.15-second response time. Works well under different lighting and background conditions. Low-cost and scalable system. Works independently without the cloud. | Processing speed decreases to 0.82 FPS during heavy computation. Detection of humans and objects is less accurate in complex backgrounds and changing lighting. | low-cost Raspberry Pi-based AI surveillance system. Uses YOLOv5 and multiple sensors to detect humans, vehicles, and animals. Provides fast and accurate real-time monitoring and alerts.

## Slide 15: LITERATURE SURVEY
Dept. of CSE-CC
AI-Based Smart Surveillance System Using Raspberry Pi and Embedded Vision B. Girirajan, S. Prabu, V. T. Thangam,
M. Sugumaran, P. Venkateshwaran, A. Kaur
Core Methodologies & Algorithms | Advantages | Limitations | Summary
DL-Assisted Access Control: Uses deep learning to evaluate access conditions over industrial controllers. Data Computation ($SMI_d$): Calculates device metrics via access limits, active controllers, and detected threats. Variation Detection: Evaluates dual input sequences ($\exists_1, \exists_2$) to track variations ($V$) against previous outputs ($PPO^*$). Schedule Verification: Dynamically grants access or reallocates controllers upon detecting anomalies or interrupts. | Reduced Failures: Minimizes controller denials, system failures, and false positives. High Consistency: Improves production consistency across human-centric Industry 5.0 systems.background conditions. Minimizes Interrupts: Mitigates adversary interruptions to maintain continuous operational schedules. . | Concurrency Limits: Facing constraints when processing simultaneous high-concurrency access requests. Data Dependency: Relies heavily on precise historical production data ($PPO^*$) for accurate anomaly detection. | Zero-Trust Access Framework: ZTN-ACS delivers deep learning-based security for Industry 5.0 operations. Continuous Verification: Monitors access requests against expected outputs to mitigate cyber threats.

## Slide 16: COMPARATIVE ANALYSIS
Dept. of CSE-CC
Paper/ Year/ Authors | Methodology | Approach | Tool/ Algorithm | Observations/Key Findings
[2] | Train a lightweight TCN using IoT/H-IoT DDoS traffic and deploy the optimized model directly on Raspberry Pi 4. | Edge-based cybersecurity and local DDoS detection. | TCN, TFLite, INT8 quantization, XNNPACK and Raspberry Pi 4. | High detection accuracy with very low inference latency and relatively low power consumption.
[3] | Fetches device MUD profiles via DHCP/LLDP and auto-generates firewall access rules. | Fetches manufacturer profiles via DHCP/LLDP and parses JSON definitions directly into per-device firewall rules. | Authenticates before connecting to hide unauthorized IoT devices. | Compact model size (675 kB), fast detection (19 ms), rapid alerts (~3 sec), multi-channel notifications (SMS/Push/Voice).
[1] | Uses an online laboratory as a practical case study for implementing ZTNA | Application/resource-level access rather than giving users unrestricted access to the entire network. | Twingate, MFA, encryption and device-security policies. | Demonstrates the practical use of ZTNA for remote educational laboratory access and highlights limitations of conventional VPN approaches.
[4] | Reviews existing remote-access/security technologies and proposes a Zero-Trust VPN framework | Combines traditional VPN connectivity with Zero-Trust access control. | OpenVPN, SSL/TLS certificates, OTP, PEP, IEP and SEP. | Provides more granular access by considering user identity, device health and authorization rather than providing broad network access after VPN authentication.
[5] | Continuously monitors client-machine state and reports unexpected changes. | Runtime trust verification rather than relying only on authentication at the beginning of a session | TPC, SWTPM and SGX-enabled SWTPM; tested using Azure and AWS. | Demonstrates runtime state monitoring and scalability testing; 128 concurrent clients were recognized within a maximum of 35.6 seconds.

## Slide 17: COMPARATIVE ANALYSIS
Dept. of CSE-CC
Paper/ Year/ Authors | Methodology | Approach | Tool/ Algorithm | Observations/Key Findings
[7] | Continuous deep learning verification for industrial controllers. | Continuously verifies access requests using deep learning instead of relying on fixed perimeter trust. | Lightweight YOLOv5 / CNNs for edge detection. | Lower system failures, fewer access denials, reduced false positives, uninterrupted schedules.
[6] | Evaluates access conditions over industrial controllers via continuous deep learning-based security verification. | Evaluates access conditions continuously over industrial controllers using deep learning models. | Evaluates real-time industrial controller requests against baseline metrics. | Minimizes controller denials, reduces system failures and false positives, and prevents adversary schedule interruptions.

## Slide 18: PROPOSED SYSTEM
Dept. of CSE-CC
SECURE REMOTE NETWORK ACCESS USING TWIN GATE AND RASPBERRY PI – Develop a secure and cost-effective remote network access system using Raspberry Pi and Twingate ZTNA.
Implement Zero Trust security with identity verification, device authentication, and least-privilege access.
Use Raspberry Pi as a lightweight network connector to securely connect internal resources to the Twingate platform.
Provide secure remote access to authorized users without port forwarding, public IP addresses, or direct exposure of internal services.
Integrate the Twingate API with Python automation to discover and dynamically register network resources with minimal manual configuration.
Support centralized management, DNS aliasing, temporary access, service accounts, activity logging, and network monitoring for secure administration and maintenance.

## Slide 19: PROPOSED SYSTEM: ADVANTAGES
Dept. of CSE-CC
Provides secure remote network access using Zero Trust Network Access (ZTNA).
Eliminates the need for port forwarding, public IP addresses, and complex firewall configurations.
Offers low-cost and energy-efficient deployment using Raspberry Pi.
Provides least-privilege access control so users can access only authorized resources.
Enables centralized management and monitoring through the Twingate platform.
Reduces manual configuration through Python-based API automation, improving scalability and efficiency.

## Slide 20: PROJECT PLANNING & SCHEDULING
Dept. of CSE-CC
Work Breakdown Structure (WBS) :
Requirement Analysis – Study the existing remote access methods, identify security limitations, and define project requirements.
System Design – Design the architecture integrating Raspberry Pi, Twingate, remote users, and internal network resources.
Raspberry Pi Setup – Install and configure the required operating system, networking components, and Twingate connector.
Twingate Configuration – Configure users, devices, resources, authentication, and access-control policies.
Python Automation – Develop and integrate the Twingate API with Python for resource discovery and automated configuration.
Testing and Documentation – Test security, connectivity, access control, automation, and performance, then prepare the final documentation and project demonstration.

## Slide 21: Methodology:
Dept. of CSE-CC
Design a Zero Trust architecture using Raspberry Pi as the network connector and Twingate for secure remote access.
Configure the Raspberry Pi and establish a secure connection with the Twingate platform.
Configure users, devices, network resources, authentication, and least-privilege access policies.
Develop a Python-based automation module using the Twingate API for resource discovery and management.
Test the system for connectivity, security, access control, performance, and reliability, followed by documentation and evaluation.
Implement DNS aliasing and temporary access permissions for flexible and controlled resource access.
Enable activity logging and network monitoring to track access, identify issues, and support secure administration.

## Slide 22: PROJECT PLANNING & SCHEDULING
The Project Schedule (The Timeline)
Dept. of CSE-CC

## Slide 23: RESOURCE/TASK IDENTIFICATION & ALLOCATION
Dept. of CSE-CC
Systematic distribution of project workload, software tools, and hardware assets
Task ID | Task Description | Primary Resource | Tools & Infrastructure | Current Status
T1: Requirements | Literature survey and system architecture design. | All Group Members | IEEE Journals, Google scholar | 100% Completed
T2:Connector & Network Setup | Raspberry Pi setup and Twingate Connector configuration. | Akshay N& Shanid Ali | Raspberry Pi, Twingate, Linux, SSH, Local Network | Not started
T3: API Automation | Python API integration and resource automation. | Akshay N | Python, Twingate API, REST API, GitHub, VS Code | Not started
T4: Security Implementation | Configure authentication and least-privilege access. | Abhishek KB | Twingate Admin Console, ZTNA Policies, DNS, Authentication & Logging | Not Started
T5: Testing & QA | System testing, bug fixing, and final documentation. | All Group Members | Postman, Twingate Logs, Word/Docs | Not Started

## Slide 24: RESOURCE/TASK IDENTIFICATION & ALLOCATION
Resource Breakdown & Project Governance
Hardware Resources
Raspberry Pi(Mini Computing Chip)
SD Card
Ethernet/Wi-Fi Router
Internet connectivity
Client Computer/Laptop
Python
Linux
Postman
GitHub
VS Code
Twingate
APIs & Services &Data Resources
Twingate API
REST API
DNS
Authentication
Activity Logs
Network Data
Software & Tools
Dept. of CSE-CC

## Slide 25: CONCLUSION
Dept. of CSE-CC
SECURE REMOTE NETWORK ACCESS USING TWIN GATE AND RASPBERRY PI provides secure and reliable remote network connectivity.
Raspberry Pi acts as a low-cost and lightweight network connector.
Twingate enables Zero Trust-based remote access without exposing internal services.
Identity verification and least-privilege access enhance network security.
Python API automation simplifies resource management and configuration.
The proposed system is scalable, cost-effective, and easy to manage.

## Slide 26: REFERENCES
Dept. of CSE-CC
[1]R. Jayadevan, S. M. Sebastian, A. Goutham, S. KV, S. T, and A. Ananthan, "Edge-Based, Power-Efficient Real-Time Wild Animal Detection and Alarm System on Raspberry Pi Using YOLO Architecture," 2025
[2]S. Naveen, R. Dhamotharan, et al., "ElephantGuardNet: A Comprehensive Solution for Elephant Conservation and Human-Elephant Conflict Reduction," Proc. ICSADL,
pp. 1470–1477, 2025.
[3]D. Ma and J. Yang, "YOLO-Animal: An efficient wildlife detection network based on improved YOLOv5," International Conference on Image Processing, Computer Vision and Machine Learning (ICICML), 2022
[4]V. Bharati, "A Deep Neural Network Machine Vision Application for Preventing Wildlife-Human Conflicts," 2021
[5]S. Gunasekara, M. Jayasuriya, N. Harischandra, L. Samaranayake, and G. Dissanayake, "A Convolutional Neural Network Based Early Warning System to Prevent Elephant-Train Collisions," IEEE, 2021

## Slide 27: REFERENCES
Dept. of CSE-CC
Jayanthi M & K.V. Kanimozhi (2025). "Enhancing the Identification of Wildlife via Self-Supervised Learning on Unlabelled Camera Trap Information"
Supreet Parida, Suvam Nayak, Anjana Mishra, Nilamadhab Mishra, Bibhu Prasad Sahoo, & Bhabani Sankar Panda (2024). “Recognizing Wild Animals from Camera Trap Images Using Deep Learning”.
Krishnaveni A & Arvinth K A (2025). "Smart Animal Monitoring System for Farms using YOLO and OpenCV"
Gabriel S. Ferrante, Felipe M. Rodrigues, Fernando R. H. Andrade, Rudinei Goularte, & Rodolfo I. Meneguette (2021). "Understanding the state of the Art in Animal detection and classification using computer vision technologies
Dr. S. V. Viraktamath, Jahnavi R, Vidya, Abhay S Bhat, & Sathvik Nayak (2021). "Wildlife Monitoring and Surveillance"

## Slide 28: REFERENCES
Dept. of CSE-CC
[11]Karthik Vasu, Anitha Premkumar, T. Ramesh, and Rajesh Natarajan, "Real-Time Tiger Intrusion Detection System Using Machine Learning and IoT" (2026)
[12]T. Manikandan, V. Nandalal, S. Joshua Kumaresan, R. Babuji, and A. Muruganandham, "IoT Based Animal Detection and Alert System for Farm Fields",2024.
[13]Sudharshan Duth P, Maneesha Shibu, and Nithyashree M, "Animal Detection in Night Light Videos Using Deep Learning",2024
[14]Prabhat Kumar Panda, Cherlopalli Srujan Kumar, Bommu Sai Vivek, Masura Balachandra, and Shashi Kant Dargar, "Implementation of a Wild Animal Intrusion Detection Model Based on Internet of Things",2022.
[15]K. S. P. Premarathna, R. M. K. T. Rathnayaka, and J. Charles, "An Elephant Detection System to Prevent Human-Elephant Conflict and Tracking of Elephant Using Deep Learning" ,2020

## Slide 29: REFERENCES
Dept. of CSE-CC
[16]AI-Based Smart Surveillance System Using Raspberry Pi and Embedded Vision B.
Girirajan, S. Prabu, V. T. Thangam, M. Sugumaran, P. Venkateshwaran, A. Kaur
[17]D. Slutskiy, Z. Jacques, N. Bazarian, S. Basnet, A. Poudel and P. Manandhar, “Non-human Primate Monitoring System: Early Alert System Against Crop Raids for Farms in Nepal,” 2024 IEEE Global Humanitarian Technology Conference (GHTC).
Diery NGOM, Alla LO, Serigne Mbacké GUEYE, Absa LECOR, "An Intelligent IoT and AI-Based Surveillance System for the Detection and Recognition of Pest Birds in Rice Crops of the Senegal River Valley"
Kathir, Balaji & Ashwini, 2024 — Animal Intrusion Detection Using YOLO v8
Curry, Trotter & McGough, 2021 – camera trap deep learning for Scottish wildcat

## Slide 30: Thank Youuuu
Dept. of CSE-CC